## Slide 1: Safe Storage of Chemicals
Phillip Crisp and Eva Crisp

## Slide 2: Chemicals in Science
Chemical Store
• Bulk chemical storage of Dangerous Goods
• Segregate Dangerous Goods according to Classes
• Original labelling according to GHS
Prep room
• Minimum chemicals, as needed
• Label Hazardous Substances* according to GHS
Laboratories
• Chemicals for immediately forthcoming experiments
• Label Hazardous Substances* according to GHS
* called “Hazardous Chemicals” in GHS

## Slide 3: What are Dangerous Goods? And what are its Classes? What is the GHS? And what do the letters mean? What are Hazardous Substances? And how do they differ from Dangerous Goods? How do we store chemicals safely?
Questions

## Slide 4: Dangerous Goods
Concept developed to allow safe transport of chemicals within and between countries
Focus on physical properties of chemicals for • fire, spillage, corrosion, toxic gas release, . . .
DGs listed in Land Transport Rule: Dangerous Goods 2005
Chemical storage is seen as a stage in the transport of chemicals, so a school chemical store must follow Dangerous Goods regulations

## Slide 5: Classes of Dangerous Goods
Class 1 Explosive substances and articles
Class 2 Gases
2.1 Flammable gases
2.2 Non-flammable, non-toxic gases
2.3 Toxic gases
Class 3 Flammable liquids
Class 4 Flammable solids
4.1 Flammable solids, self-reactive substances, polymerizing substances
and solid desensitized explosives
4.2 Substances liable to spontaneous combustion
4.3 Substances which, in contact with water, emit flammable gases
Class 5 Oxidizing substances and organic peroxides
5.1 Oxidizing substances
5.2 Organic peroxides
Class 6 Toxic and infectious substances
6.1 Toxic substances
6.2 Infectious substances
Class 7 Radioactive material
Class 8 Corrosive substances
Class 9 Miscellaneous dangerous substances and articles

## Slide 6: Rules for Dangerous Goods
Packaging of chemicals appropriate to the potential hazard Packing Groups: I > II > III
Labelling for transport Dangerous Goods Diamonds, placarding, etc
Segregation of Classes and Subclasses depending on reactive hazards by distance + secondary containment, e.g. cabinets, tubs
Minor storage <Placarding quantity < Manifest quantity
Chemical register (for minor storage) = list of hazardous substances at each storage location, usually with quantities, DG Classes and SDSs

## Slide 7: GHS Globally Harmonized System of Classification and Labelling of Chemicals*
Developed to protect people from harm when using chemicals
Classification system for chemicals that pose • Physical hazards • Health hazards • Environmental hazards
A chemical that satisfies one or more hazard criteria is classified as a Hazardous Chemical (GHS) = Hazardous Substance (NZ)
Labelling+SDSs required to advise people of hazards
*United Nations "Globally Harmonised System of Classification and Labelling of Chemicals (GHS)" 11th ed., 2025.

## Slide 8: Dangerous Goods vs Hazardous Substances
All Dangerous Goods are Hazardous Substances
Not all Hazardous Substances are Dangerous Goods
Hazardous Substances must be listed in the Chemical Register (which comprises DGs + non-DG HSs)
List of Dangerous Goods is almost static.
List of Hazardous Substances is continually updated as new data become available
European Chemicals Association (ECHA) is the most extensive data source for classifications of Hazardous Chemicals, c.f. NZ EPA classifications

## Slide 9
Chemical Store
• Location
• Door
• Bund
• Lighting
• Shelving
• Ventilation
• Electrical equipment
• Layout
• Ergonomics
• Safety Data Sheets
• Safety equipment
• Segregation
• Storage cabinets
• Housekeeping
See “Chemical storage in Science” https://www.riskassess.com.au/docs/ChemicalStorageInScience
See “Safety and Science”, chapter 20 (2023)
Risk Management Plan for Class 3, 4 and 5 DGs
HSW (Hazardous Substances) Amendment Regulations 2026

## Slide 10
3
8
4.3
5.1
9
6.1
6.1
6.1
6.1
4.1
Air
Light
& fan
switches
SDSs
Bund
6.1
PREP ROOM
Air
Spills kit
PREP ROOM

## Slide 11: Segregation of chemicals
• Segregation by Class/Subclass (then alphabetical or by group)
• Flammable liquids (Class 3) and Corrosives (Class 8) in cabinets, far from door
• Chemicals that release flammable gases (Class 4.3) in dry, ventilated box or cabinet
• Secondary containment (tub, glass/ceramic tray) if <3 m separation
• Incompatible chemicals not above each other
• Liquids not above solids

## Slide 12: Storage cabinets for DG Classes
• Essential: Flammable Liquids and Corrosives Others: if sufficient quantity and space
• Plastic better than metal for Corrosives
• Bund at bottom of cabinet (25% total capacity)
• Avoid HCl and NH3 in same cabinet
• Plastic coated bottles preferred for HNO3, H2SO4
• Spark-proof fan for safe ventilation
• Flammable Liquids and Corrosives cabinets furthest from door to allow emergency escape

## Slide 13: Housekeeping in the chemical store
• Non-Dangerous Goods not in chemical store, unless sufficient space.
• Most smell due to leakage of vapour around lid seals. Tighten lids of volatile acids and organic chemicals, but not if chemical releases a gas
• No chemicals on floor
• Check extremely hazardous chemicals, e.g., sodium metal, every few months

## Slide 14
Prep room
• Return Dangerous Goods to chemical store as soon as possible
• GHS labelling of decanted or transferred hazardous chemicals
• NEVER use food containers NEVER put chemicals in a food refrigerator
• No ignition sources near flammable liquids
• Store chemical wastes as DGs
• Keep locked when no staff present

## Slide 15
Laboratories
• Chemicals for immediately forthcoming experiments only
• Good ergonomics
• Labelling according to GHS
• Separate chemical waste containers for each heavy metal, non-halogenated organics, . .
• Keep locked when no staff present

## Slide 16
Help from RiskAssess
• Identification of Dangerous Goods
• Standard handling procedures
• Understanding potential hazards
• Labelling of chemicals according to GHS
• Labelling of chemical wastes
• Chemical inventory and chemical register with SDS management

## Slide 17: DEMONSTRATION
• Learning resources
• Examples
• Labelling, inc. chemical wastes
QUESTIONS
team@riskassess.co.nz