## Slide 1: RiskAssess New Features Chemical Disposal, Tips & Tricks
Phillip and Eva Crisp

## Slide 2: New features

## Slide 3: Databases
Added 171 chemicals and solutions
163 equipment items
74 biological/food items
Improved advice:
300+ items

## Slide 4
Notes: Learning resources, videos & faq. And Phillip’s book!

## Slide 5
Notes: Fully signed, but lots of other things like stats, high risk etc

## Slide 6
https://www.riskassess.com.au/info/student_resources
Notes: New resources, classroom video, blooket & quiz for students

## Slide 8: Chemical storage in science Advice for: • chemical store • prep room • student laboratories Design, storage arrangements, segregation, ventilation, specific chemical advice, labelling, housekeeping, etc https://www.riskassess.com.au/docs/ChemicalStorageInScience.pdf 15 page document

## Slide 9: Chemical inventory and chemical register with SDS management QR codes stocktaking on phone

## Slide 10: Chemical disposal

## Slide 11: The law
Follow local regulations for disposal of wastes to sewer and garbage, rather than the advice in RiskAssess.
Retain wastes for collection by a waste collection service, if not allowed to put down drain or in garbage
Inland waters usually have special requirements.

## Slide 12: Disposal advice
Disposal advice in RiskAssess:
• provides a ‘default’, when no other advice is available
• prioritizes safety
• minimizes harm to the environment
• offers a responsible approach to student learning.

## Slide 13: RiskAssess Advice
Individual chemical advice in ‘Disposal’ for each of 3000+ chemicals and solutions
‘Disposal of chemical wastes’ https://www.riskassess.com.au/docs/DisposalOfChemicalWastes.pdf
‘Chemical waste containers’ https://www.riskassess.com.au/info/waste_containers
‘Labels for Chemical waste containers’ https://www.riskassess.com.au/info/waste_container_labels
‘How to dispose of chemical wastes’ In: ‘Safety in Schools’ book, chapter C7

## Slide 14: Chemical Disposal
The quantity of chemical wastes generated in a school is very small compared with industry, agriculture, mining, etc.
HOWEVER
• A school is an educational institution
• Attitudes adopted during youth continue into adulthood
• Proper training should be given to those who will later be decision makers

## Slide 15: The improvement process
eliminate unwanted chemicals
redesign procedures to minimize waste production, e.g. spot reactions, recycling, destruction, less toxic chemicals
dispose of wastes LEGALLY SAFELY by - sewer - garbage - waste collection service

## Slide 16: Chemical wastes in schools
Aqueous liquid wastes
• dissolved salts
• acidic or basic
• suspended particles
Water-miscible organic wastes
alcohols, e.g. methylated spirits
ketones, e.g. acetone
Water-immiscible organic wastes
• hydrocarbons, e.g. hexane, kerosene
• special chemicals, mostly for organic chemistry
Solid wastes
• precipitates, e.g. BaSO4, Fe oxides
*

## Slide 17
Problems in the sewer!
• toxic metals
e.g. Hg, Cd, Pb, As, . . . VERY BAD Cu, Ni, Co, . . . BAD since contaminate sludge $$$
• toxic persistent organic chemicals
e.g. pesticides since contaminate sludge $$$
• highly acidic/alkaline liquids since may damage pipes
• flammable liquids (water-immiscible) since may cause an explosion!

## Slide 18
Aqueous liquid wastes
Pour down the sewer ONLY if the criteria of the water authority are met.
Otherwise, an environmentally responsible approach:
• neutralize to ~pH 6.5-8.5 (natural waters)
• only “safe” amount of each chemical down the drain
in order to minimise environmental harm from treated sewage when it is released into river or ocean.
All wastes exceeding a “safe” amount of a chemical should be retained for a waste collection service.
WHAT IS SAFE?

## Slide 19: Estimation of “safe” quantities*
Consider the cation and anion in a salt separately.
Toxicity of a salt is dominated by the most toxic ion:
e.g. lead chloride, potassium dichromate
Some ions should not go down the drain at all
e.g. Hg2+, Pb2+, Cd2+, . . .
while others are OK almost without (school) limit
e.g. Na+, Ca2+, Cl-, SO42-, . . .
and other ions in between
* RiskAssess “Disposal of chemical wastes”, in Learning Resources

## Slide 20: Tabulation and calculation
“Safe” disposal quantity for an ion for a class:
0 – 1000 g/day
Copper sulfate
copper: 1 g/day [Very toxic to aquatic life
with long lasting effects]
sulfate: 1000 g/day. [In solid laundry detergent]
Therefore, copper sulfate: 1 g/day (as solid or solution)
Enough for some spot tests down the drain.
Beyond that, wastes need to be collected!

## Slide 21: Organic liquid wastes
Water-miscible
e.g. methylated spirits, acetone
Dilute 1 part to 20 parts water, then down the drain.
Prevents explosive air/vapour mixture.
Microorganisms in sewer will consume the chemicals.
Water-immiscible
e.g. hexane, kerosene
Retain for collection by waste service.
Separate hydrocarbon waste from halogenated waste.

## Slide 22: Waste processing
Collection
Large bottles (e.g. 2.5 L ‘Winchesters’) correctly labelled, funnel at top (fume cupboard)
Treatment
Only if time and skilled people available
Disposal
To maximum recommended daily quantity:
• down the drain or into garbage
Otherwise, retain for waste collection
SEPARATE CONTAINER FOR EACH WASTE!

## Slide 23: Solid wastes
Only “material of a domestic nature”
is allowed to be disposed of in the garbage
Consider
transport of garbage
leaching from landfill
Geologically-stable minerals
(precipitated during reactions)
e.g. barium sulfate (baryte)
No leaching of toxic chemicals in a domestic landfill.

## Slide 24: Purpose of disposal advice
• assists decision making
• promotes safe disposal techniques
• focuses on avoiding serious environmental harm
• reduces the cost of waste collection service
• decreases emphasis on less harmful substances
• provides a learning tool for staff and students
• promotes care for the environment

## Slide 25: Tips & Tricks

## Slide 26
Shortcuts
icons, hcl, part name, click banner,
links, hot links, delete,
Best RAs
Scheduling
Excel/csv, any dates, last week,
search, no# pracs, prep notes,
double booking, lodged date
Tools
customise year groups,
stocktaking & usage, invoice,
backup system, defaults
Resources
learning resources, faq, eBook,
videos, libraries: Stile+EP+Edrolo+
Jacaranda
Labels
standard, custom & waste labels,
multiple chemicals on sheet,
mixtures, non-chemicals,
free text, biohazard symbol
Operations
author’s update vs modifiable copy,
reschedule, archive risk
assessments, annual review,
tech-only RAs, review notes,
high/extreme: 3 signatures, list,
disposal info
Student RiskAssess
view student PINs, not last year
multiple prac management
Chemical inventory/register
QR codes, stocktaking on phone